## Slide 1
Project A1
big.LITTLE Heterogeneous Multi-Core SoC
RISC-V based design and verification project
2× P-Cores RV32IM · 5-stage
2× E-Cores RV32I · 3-stage
Shared memory MSI coherence
Optional ASIC → GDSII
Scope: RTL design, simulation, verification and synthesis/physical-design exploration. FPGA implementation is excluded.

## Slide 2
1. Problem statement & project goal
Why heterogeneous compute?
2
One core type cannot optimize both performance and energy.
High-performance cores are fast but consume more dynamic power.
Small efficiency cores reduce energy for light or background work.
A common ISA and coherent memory let software move work between both.
The project demonstrates this trade-off in an implementable RISC-V SoC.
Goal: a 4-core asymmetric SoC
P-cluster Latency / throughput
E-cluster Energy efficiency
Shared L2 + coherent memory

## Slide 3
2. Scope, assumptions & measurable outcomes
A focused A1 build — no Project A2 peripherals or FPGA deployment
3
IN SCOPE
RV32I E-Core and RV32IM P-Core
Private L1 caches + shared inclusive L2
MSI snooping coherence
Migration controller and clock-gating control
Simulation, regressions, coverage and optional formal checks
OUT OF SCOPE
Project A2 UMA fabric
ML accelerator and DMA
FPGA board integration
Production tape-out commitment
SUCCESS CRITERIA
RISC-V ISA regressions pass
Coherent producer–consumer test passes
State-preserving P↔E migration
Synthesis reports; physical flow to GDSII if schedule permits

## Slide 4
3. Top-level SoC architecture
All modules communicate through a simple coherent system fabric
4
P-Core 0 RV32IM
P-Core 1 RV32IM
E-Core 0 RV32I
E-Core 1 RV32I
Private L1 I/D caches P: 16 KB 2-way WB | E: 8 KB direct-mapped WT
Coherent Interconnect + MSI snoop bus
Shared L2 cache 64 KB · 4-way · inclusive
SRAM / Boot ROM main memory model
UART
IRQ ctrl
Migration + Power Manager

## Slide 5
4. Heterogeneous core microarchitectures
Same ISA family, deliberately different cost/performance points
5
Efficiency Core — RV32I · 3-stage
FETCH PC · I-Mem
DECODE / REG RD Decode · RegFile
EXEC / MEM / WB ALU · D-Mem
Static not-taken branch policy; simple forwarding and load-use stall.
Smallest area/power target for low-intensity work.
Performance Core — RV32IM · 5-stage
IF I$ · BHT
ID Decode · RF
EX ALU · MUL/DIV
MEM D$
WB Writeback
Full forwarding; 256-entry 2-bit BHT + BTB; iterative M extension.
Counters: cycles, retired instructions, branch/cache misses.

## Slide 6
5. Memory hierarchy & MSI cache coherence
Private L1 speed with shared-data correctness
6
P-cluster L1 16 KB · 2-way · write-back
E-cluster L1 8 KB · direct map · write-through
Snoop / coherence bus BusRd · BusRdX · BusUpgr
Shared L2 64 KB · 4-way · inclusive
SRAM
MSI line states
I Invalid
S Shared
M Modified
Read miss: I→S. Write miss/upgrade: I/S→M. Snoops invalidate or flush dirty data when ownership changes.
Snooping is practical for this 4-core project.
L2 snoop filter tracks L1 sharers.
Start with one outstanding miss/core to keep control logic manageable.

## Slide 7
6. Task migration & power-management approach
Hardware-assisted, software-controlled migration policy
7
IDLE
wait for event
SAVE
32 regs + PC + key CSRs
TRANSFER
migration buffer
RESTORE
load destination
DONE
resume task
Triggers IPC threshold · software CSR · power budget
Safety actions quiesce core · flush/confirm state · atomic hand-off
Power control per-core clock enable · wake-on-interrupt · DVFS stub
Design rule: the architecture preserves architectural state and resumes at the saved PC; basic control is exposed through memory-mapped CSRs.

## Slide 8
7. Module interfaces — how the blocks link
Keep the top level testable by defining clean, narrow interfaces
8
Core ↔ L1 cache
instruction/data request, address, byte enables, response, stall
L1 ↔ coherent fabric
miss request, refill/writeback, snoop command, ack/data
Fabric ↔ L2/SRAM
address decode, arbitration, read/write channel, response
Migration manager ↔ cores
halt/ack, register-state port, resume PC, interrupt routing
CSRs ↔ software
memory-mapped control, status, performance counters, IRQ enable
Recommended implementation order: define interfaces and standalone test benches before integrating the adjacent module.

## Slide 9
8. Required parts & software toolchain
All deliverables are RTL- and verification-focused
9
RTL / design components
SystemVerilog RTL: cores, caches, MSI controller, fabric, migration/power blocks
Boot ROM + synthesizable SRAM models
RISC-V bare-metal startup code and linker script
Memory-mapped UART / interrupt-controller models for system tests
Software tools
Verilator — fast linting, simulation and coverage
GTKWave — VCD/FST waveform inspection
RISC-V GCC / binutils — bare-metal test programs
Yosys — synthesis and area estimates
SymbiYosys + riscv-formal — optional formal properties
OpenROAD / OpenLane — optional RTL-to-GDSII exploration
Version control: Git + Makefile-based repeatable regressions. FPGA tools are intentionally not required.

## Slide 10
9. Verification strategy
Verification grows from small blocks to full system behavior
10
1
Unit tests
ALU · decoder · regfile · cache FSM · arbiter · migration FSM
2
Module integration
core + L1 · fabric + slaves · L2 refill/writeback
3
Subsystem tests
coherence ping-pong · contention · migration sequences
4
System regression
boot · multi-core programs · UART output · performance counters
Key checks: rv32ui / rv32um ISA tests, hazard tests, cache writeback, MSI producer–consumer, false sharing, migration state preservation and random traffic stress.

## Slide 11
10. Design and verification flow
A gated flow minimizes integration risk
11
Specify
ISA subset, cache parameters, interfaces
Implement
module RTL + assertions
Simulate
directed tests + waveforms
Integrate
adjacent blocks, then SoC top
Regress
ISA tests + system scenarios
Measure
coverage, IPC, misses, synthesis
Exit gate: core ISA tests + hazards pass
Exit gate: memory cache + MSI tests pass
Exit gate: SoC boot + migration pass
Do not begin physical design until the RTL regression is stable. Preserve reports and waveforms as project evidence.

## Slide 12
11. Milestone plan
Prioritize a credible verified MVP before advanced features
12
M1 · Foundation
ALU, regfile, decoder, test infrastructure
Week 1
M2 · E-Core
3-stage RV32I + rv32ui regression
Weeks 2–4
M3 · P-Core
5-stage RV32IM, BHT/BTB, rv32um
Weeks 5–7
M4 · Memory
L1/L2 + MSI coherence tests
Weeks 8–11
M5 · System
integration, migration, power controls
Weeks 12–14
M6 · Closure
full regression, synthesis; optional GDSII
Weeks 15–16+
MVP fallback: one E-Core + one P-Core, simple L1 caches, SRAM, UART, and no migration/coherence optimizations. Expand only after this is stable.

## Slide 13
12. Optional ASIC implementation flow — only if time permits
An exploration flow, not a tape-out promise
13
Verified RTL
frozen regression
Synthesis
Yosys / constraints
Floorplan
area, IO, power grid
Place & route
OpenROAD/OpenLane
Sign-off checks
DRC/LVS/STA review
GDSII
final layout artifact
Inputs required: synthesizable RTL, SDC timing constraints, standard-cell/PDK collateral and validated memory macros.
Report area, timing and power estimates honestly; use a supported open PDK only if the environment and schedule allow.
Primary academic deliverable remains a verified RTL design and documented results.

## Slide 14
13. Expected deliverables
What the completed project presentation and repository will show
14
Architecture
top-level block diagram, core/cache/migration microarchitecture
RTL
clean SystemVerilog hierarchy with documented interfaces
Verification
test plan, regressions, waveforms, coverage/formal results
Evidence
benchmark counters, cache/coherence and migration demonstrations
Implementation
synthesis reports; optional physical-design/GDSII artifacts
Final message: build a verified heterogeneous RISC-V SoC in deliberate stages; treat physical design as an optional final extension.